## Slide 1: What’s A Hazard and What’s Not
By
Bruce Blackwell, BA Blackwell & Associates Ltd.
Credit: Gwen Shrimpton, Vegetation Management, BC Hydro/BCTC

## Slide 2: Objectives:
Educate about fire hazards and liability related to vegetation management
Overview of Fuels Research Project
Introduce Fire Hazard Rating System

## Slide 3: Outline
Why Manage Hazardous Fuels?
Wildfire Regulation Section 10:
“A person carrying out an industrial activity that is a utility transmission operation, on or within 300 m of forest land or grass land, must maintain the site in a manner that prevents any fire from spreading from the site.”
Vegetation managers must be able to differentiate benign fuels from those that constitute a liability.

## Slide 4: Basic Fire Theory
Measures of Fire Behaviour
Fireline Intensity
Rate of Spread
Weather Effects
Wind Speed
Fuel Moisture
Temperature

## Slide 5: Basic Fire Theory
Rank | 1
Rate of Spread (m/min) | nil
Fireline Intensity (kW/m) | <10
Description | Smouldering ground or creeping surface fire
Qualitative Fire Behaviour | These fires have no open flame and produce white smoke
Response to Control Efforts | Firebrands and going fires tend to be virtually self-extinguishing unless high DC and/or BUI values prevail, in which case extensive mop-up is generally required.
Fire Intensity Rank
http://bcwildfire.ca/fightingwildfire/firerank.htm

## Slide 6: Basic Fire Theory
Rank | 2
Rate of Spread (m/min) | <1.5
Fireline Intensity (kW/m) | 10-500
Description | Low vigour surface fire
Qualitative Fire Behaviour | These fires produce visible open flame; have little or no spread, and have an unorganized flame front
Response to Control Efforts | Direct manual attack at fire's head or flanks by fire fighters with hand tools and water possible. Constructed fire guard should hold.
Fire Intensity Rank
http://bcwildfire.ca/fightingwildfire/firerank.htm

## Slide 7: Basic Fire Theory
Rank | 3
Rate of Spread (m/min) | 1.5-3.0
Fireline Intensity (kW/m) | 500-2000
Description | Moderately vigorous surface fire
Qualitative Fire Behaviour | Vigorous surface fire with a moderate rate of spread. They have an organized front and may display "candling", which is when a tree's fuels ignite and flare up, along the perimeter and/or within the fire
Response to Control Efforts | Hand-constructed fire guards likely to be challenged. Heavy equipment generally successful in controlling fire.
Fire Intensity Rank
http://bcwildfire.ca/fightingwildfire/firerank.htm

## Slide 8: Basic Fire Theory
Rank | 4
Rate of Spread (m/min) | 3 to 6
Fireline Intensity (kW/m) | 2000-4000
Description | Highly vigorous surface fire, torching (or passive crown fire).
Qualitative Fire Behaviour | Grey to black smoke, has an organized surface flame front, and has a moderate to fast rate of spread along the ground. Short aerial bursts and short range spotting will occur with these fires
Response to Control Efforts | Control efforts at fire's head may fail.
Fire Intensity Rank
http://bcwildfire.ca/fightingwildfire/firerank.htm

## Slide 9: Basic Fire Theory
Dead Fuel Diameter Classes
1-hour time lag fuels
  (< 0.625 cm diameter)
10-hour timelag fuels
  (0.625 - 2.5 cm diameter)
100-hour timelag fuels
  (2.5 cm - 7.6 cm diameter)
1000-hour timelag fuels
  (> 7.6 cm diameter)

## Slide 10: BC Hydro Fuels Research Project
Study Sites
18 study sites
Located between Squamish and Lillooet
Wide range of conditions

## Slide 11: Fuel Types
Fuel Conditions in the study area
Standing Fuels
Slash Fuels

## Slide 12: Fuel Types
Fuelbed Type A (Light-Medium slash)

## Slide 13: Fuel Types
Fuelbed Type B (Heavy Slash)

## Slide 14: Fuel Types
Fuelbed Type C (Tall Shrubs/Deciduous)

## Slide 15: Fuel Types
Fuelbed Type D (Coniferous)

## Slide 16: Fuel Types
Fuelbed Type E (Mixed)

## Slide 17: Fuel Loading

## Slide 18: Fuel Loading

## Slide 19: Hazard Rating
Purpose:
Objective and consistent means of assessing Fire hazard
Prioritize fuel treatment efforts
Assess effectiveness of treatments
Build understanding of factors affecting fire hazard

## Slide 20: RoW Hazard Rating—Fuels
*1Flammable fuel is defined as: Lichens, evergreen shrubs, pinegrass, juniper or scotch broom.
*2 If (3)fine woody fuel continuity is less than 50% (level A, B, or C) then (4) large woody fuel continuity is scored level A.
*3 Deciduous Crown Closure is only a factor in conifer dominated stands. If (5) Conifer Crown Closure is 40% or less (level A or B) then (6) Deciduous Crown Closure is scored level A.
*4 If (5) coniferous crown closure is less than 20% (level A), then (7) "Conifer crown base height" and (9) "coniferous forest health" is scored level A.

## Slide 21: RoW Hazard Rating—Environment
*5 If (11) Slope is less than 30% (level A or B) then (12) aspect is considered flat (level C).

## Slide 22: RoW Hazard Rating

## Slide 23: Treatments
Treatments
Pile and burn (PB)
Standing Mow (STM)
Downed Mow (DM)
Chip (CH)

## Slide 24: Treatment Outcomes

## Slide 25: Treatment Outcomes

## Slide 26: Treatment Outcomes

## Slide 27: Treatment Outcomes

## Slide 28: Treatment Outcomes

## Slide 29: Conclusions
Take-home messages:
Amount of fuel is not as important as the type and distribution of fuels
Hazards exist in both standing and downed vegetation
Fuel management should focus on fine fuels (<7cm)
Management should discourage conifers and encourage deciduous shrubs
Purpose of management is not to prevent fire, but to prevent damage to infrastructure and adjacent values.
Vegetation management and fuels management go hand in hand.
Fuel-free zones can reduce fuel treatment costs in the rest of the RoW.